## Slide 1: Wireless Embedded Roadway Health Monitoring (WERHM)
Advisers:
Dr. Daji Qiao
Dr. Jiming Song
Dr. Tie Qiu
Jeramie Vens
Members:
Brandon Wachtel
Johnnie Weaver
Trieu Nguyen
Chris Sheafe
Brandon Maier
Mitch Balke
Tyler Fish
Client:
Dr. Halil Ceylan,
Department of Civil, Construction and Environmental Engineering

## Slide 2: Scope of the Project
What are we doing?
Why are we doing it?
Past efforts

## Slide 3: Scope - What are we doing?
Creating a network of nodes that measure humidity and temperature within roadways
Requirements of the network are:
  Wireless communication between nodes and a base station that stores data
  Low power consumption for extended life
  Able to withstand harsh environment- temperature, chemicals, stress, etc.
  Node size must be small enough to minimize impact on road integrity.

## Slide 4: Scope - Why are we doing it?
Wireless Communication
Provides a feasible method of monitoring the status of roadways and other structures throughout their lives
Directly observes the condition of the roadway at different parts as often as desired
Determines more accurately when a roadway needs to be replaced

## Slide 5: Scope - Past Efforts
Wired Communication
  Delicate-Connections destroyed during pouring and curing process of concrete
Wireless Communication using Zigbee operating at 2.4GHz
  High power consumption- surviving nodes died within a few days

## Slide 6: Current Design
Software/Networking
Hardware
Power Transfer
Charging
Battery
Enclosure
Base station

## Slide 7: Current Design - Software/Networking
Wireless Sensor Network utilizes directed flooding technique
All software optimized for low power consumption, very low active duty cycle

## Slide 8: Current Design- Hardware
Powered by MSP430F2122 MCU
4 Mbit serial flash storage
RTCC for accurate timekeeping
Overall size 1 1/8” x 2 1/8"
Alternate design includes battery charging circuitry
Non-Charging PCB

## Slide 9: Current Design - Hardware
PCB w/Charging

## Slide 10: Current Design - Power Transmission
Power transmitter
    Based on Royer Oscillator circuit with 12 VDC power supply
    Transmission frequency depends on LC tank of the circuit
      Current resonant frequency is 2.189 MHz

## Slide 11: Current Design –Power Receiver
Single 2-in square coil
Frequency matching by adding capacitor(s).
  Best efficiency

## Slide 12: Current Design - Charging
The charging circuit shall be based around Linear Technologies LTC4121.
The input is 4.2V – 40V and 400mA.
This chip was chosen based upon a phone conference with a LTC representative
The chip can be found here. http://www.linear.com/product/LTC4121

## Slide 13: Current Design – Battery
= 2629.73 Days
= 7.20 Years
900 mAH Lithium-Ion Rechargeable Battery
Equation based from Digikey.com

## Slide 14: Current Design - Enclosure
Two enclosure designs
3-D printed using ABS plastic
  Acrylonitrile Butadiene Styrene
Needs to withstand the heat, pressure, and acidity of curing concrete

## Slide 15: Current Design - Base station
Base Station is the system’s access point
    Collect readings from network
    Configure run-time settings
Starts network setup and configuration
General-purpose computer with transceiver
    Adaptable to different use-cases
    RaspberryPi B+ with a CC1101

## Slide 16: Challenges
Wireless Charging
Network Routing
Miscellaneous

## Slide 17: Challenges - Charging
Charging through concrete
Charging range
  Up to 8 inches
  Efficiency rapidly decreases
Size of the coils
  Approx. 2” square
  results in a very small amount of magnetic flux

## Slide 18: Challenges - Network Routing
Wireless ad hoc network
    Network decentralized and topology unknown
Custom version of flooding
    Nodes broadcast packet in direction of Base station
    Simple, but not optimal
Network must survive failing nodes

## Slide 19: Challenges - Miscellaneous
Size constraints require reflow assembly
  Lack of experience
Sensor Exposure
  Expose the sensor indirectly to the concrete environment
Temperature
  Exposure to Iowa summer/winter temperatures
  Ranging from -20 F to 140 F

## Slide 20: Test Plan
Network Routing & Communication
Power Transmission
Charging Battery
Enclosure

## Slide 21: Test Plan - Network Routing/Communcation
Test data integrity in multi-hop network
  In and out of concrete
Test network resilience to node failures
Texas Instruments CC1101 RF Transceiver
433 MHZ frequency selected for propagation through concrete

## Slide 22: Test Plan - Power Transmission
Test circuit through air then concrete
  Measure efficiency and compare
Load Analysis
  100 Ohms ideal for maximum efficiency
  Efficiency based off power input vs output

## Slide 23: Test Plan - Charging Battery
Testing of the charging circuit will be in two steps.
  Charging with a Benchtop DC power supply as the source.
  Charging with inductive coils as the source.
For both tests, a NI MYDAC will capture the charging curve.
Wireless Charging

## Slide 24: Test Plan - Enclosure
Waterproof Test
  Submerge enclosure in water
  Remove from water and checked for moisture in enclosure
Weight Test
  Used a flat surface to distribute weight
  Place weights on each side
Nylon Mesh Covering
Sensor Retrieved After Burial

## Slide 25: Scenarios we Thought / Accounted For
Temperature Ranges
Loss of Power (Battery Dies)

## Slide 26: Scenarios - Temperature Ranges
LI-ION battery Operating Temperatures
    Charging Range: 32 ⁰F to 113 ⁰F
    Discharging Range: -20 ⁰F to 140 ⁰F
    No charging below freezing.
    Better efficiencies at higher temperatures.
    http://batteryuniversity.com/learn/article/charging_at_high_and_low_temperatures
All other components fall roughly within the LI-ION’s operating temperature range.

## Slide 27: Scenarios - Loss of Power (Battery Dies)
If the Battery dies (Falls below 1.2V)
  Shutdown mode of charging chip (LTC 4121)
    Disconnect the battery from the circuit.
    Prevents battery damage
    Upon recharge chip will reconnect the battery
Battery disconnect does not delete stored data
The node ID and system time will be retained

## Slide 28: Questions?
Wireless Communication
Sensor Retrieved After Burial
Thank You